## Slide 1: Lifetime Denoising
Varun Mannam
EE department, University of Notre Dame
01/01/2020

## Slide 2: Outline
Motivation and Noise type
Options for lifetime denoising
Block diagram at high level and low level
Preprocess and post-process
Results and metrics to compare
Conclusions

## Slide 3: Motivation
Lifetime provides the additional contrast to the fluorescence intensity since it is independent of so many factors like power, concentration, movement of the animal etc.
But the lifetime information is noisy with low-SNR.
Only our setup has the lifetime information extraction capability.
To get high SNR, lot of averages are required with in the same FOV, which takes more time and can affect photobleaching of the sample.
Use machine learning model to perform lifetime denoising like the intensity denoising [1], but the lifetime noise type is not same as intensity noise (which is combination of Poisson noise and Gaussian noise) [2].
[1] Zhang, Yide, Yinhao Zhu, Evan Nichols, Qingfei Wang, Siyuan Zhang, Cody Smith, and Scott Howard. "A poisson-gaussian denoising dataset with real fluorescence microscopy images." In Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition, pp. 11710-11718. 2019.
[2] Zhang, Yide, Aamir A. Khan, Genevieve D. Vigil, and Scott S. Howard. "Investigation of signal-to-noise ratio in frequency-domain multiphoton fluorescence lifetime imaging microscopy." JOSA A 33, no. 7 (2016): B1-B11.

## Slide 4: Lifetime noise type observations
SNR of estimated lifetime is the ratio of mean lifetime and standard deviation of lifetime
For Poisson dominated noise (ex: intensity), mean of noise is and standard deviation of noise is which gives the SNR value is =
where is the number of detected photons. (i.e., , and and )
From JOSA paper, is also inversely proportional to ,
so we can assure that lifetime noisy type is also Poisson dominated
noise with additional factor of true lifetime value.
Also, from the F value which is independent of , this also
confirms that lifetime has Poisson dominated noise distribution.

## Slide 5: Options for machine learning lifetime denoising
Option1: Train the network from scratch with lifetime image dataset
  Need to capture the lot of images → only our setup has lifetime imaging capability
  Creation of dataset takes longer time and photobleaching on the samples for longer acquisitions
  Can not cover all the microscopic modalities like in intensity denoising (widefield and confocal are missing here)
  Need of image registration to get the ground-truth image in each FOV (stage movement is more)
  Cells types are limited to only BPAE, mouse kidney and mouse brain here for fixed wavelength (800 nm): Zebrafish has lot of auto-fluorescence at 800nm.
  Training a new model takes lot of time to find best tuning parameters (like learning rate, optimizer, machine learning NN model (ex: U-Net/noise2noise model)).
  Evaluation metrics and comparison with other methods takes more time.

## Slide 6: Cont
Option2: Use the existed intensity denoising network (even the lifetime noise is not combination of Poisson and Gaussian noise) and test the lifetime denoising performance
  Only inference is used here: collection of dataset and model training is avoided here
  Use the two-photon microscopy fixed cells (BPAE and mouse kidney)
  Possible with zebrafish samples (later)
  Use the pre and post process steps to convert the lifetime images for the network input and output
  Evaluation metrics are required, i.e., the ground truth lifetime is required which can be obtained by averaging the samples with in the same FOV.
  To get the ground truth image, image registration is required if the stage movement is more with in the same FOV.

## Slide 7: Lifetime denoising: Option2
High-level block diagram of lifetime denoising is here
Image
denoising (Noise2Noise)
Noisy
Lifetime
denoised
Lifetime
Low-level block diagram of lifetime denoising is here
Image
denoising (Noise2Noise)
Noisy
Lifetime
denoised
Lifetime
Pre
process
Post process
limit the lifetime from 0 to 10nsec.
restore the lifetime between 0 to 10nsec and use 1-4nsec in display of HSV image
Read
.tif file
mat
file

## Slide 8: Cont..
Preprocess step: replace the pixels whose lifetime is above 10nsec and below 0nsec with 0nsec save to a .tif file or read the .tif file and limit lifetime values between 0 to 10nsec (valid range) in python.
In mouse kidney, the number of pixels within the valid range is 98% and less than 2% is out of the range and in BPAE cells, the number of pixels within the valid range is 60% and around 40% is out of the range.
Divide the lifetime image by 10e-9 to get the image with in 0-1 range and passthrough the network for the denoised image
Postprocess step: add the value of 0.5 and multiply with 10nsec to get the denoised lifetime image. (within valid range)
Use the lifetime of 1-4nsec to display the results in HSV mode.

## Slide 9: Image registration
Small PSNR improvement is observed in the denoised result, since to the target image is also noisy due to the stage movement.
Image registration is required to align the images by correcting the stage movement.
methods:
  Register virtual stack -> imageJ (need input of valid range)
  Correct_3D_drift -> imageJ (need input of valid range)
  imregister -> Matlab (need input of valid range)
We used Matlab based image registration function (imregister()) with parameters: [optimizer, metric] = imregconfig(‘monomodal’) (all images are captured using the same sensor)
Where optimizer: RegularStepGradientDescent and Properties: GradientMagnitudeTolerance: 1.000000e-06 -> epsilon value to say it is reached the convergence, MinimumStepLength: 1.000000e-06 -> lr_min (1e-8), MaximumStepLength: 1.000000e-02 -> initial lr -> 1e-3, MaximumIterations: 500 -> number of iterations (epochs), RelaxationFactor: 1.000000e-01 -> learning rate (eta) and metric is MSE.

## Slide 10: BPAE samples dataset

## Slide 11
Results: Noisy and denoised images (HSV)
Full frame
ROI

## Slide 12: Results: Metrics and comparison
Figure: PSNR of the lifetime images in the same FOV
Image | PSNR (dB) on the HSV data | SSIM (Structural Similarity index)
Noisy lifetime image | 8.0485 | 0.0774
Denoised lifetime image (at index 43) | 9.8047 | 0.1066
difference in PSNR is 1.7561 dB
power is decreased as time progress -> shift in Z plane
Average (over 50 image) input PSNR = 8.2068 dB, denoised PSNR = 9.9311 dB with average difference of 1.7243 dB

## Slide 13
Results: Noisy and denoised images (HSV)
(with registration)
Full frame
ROI
Why the artifacts as red cells in denoised image within the ROI?

## Slide 14: Results: Metrics and comparison
Figure: PSNR of the lifetime images in the same FOV
Image | PSNR (dB) on the HSV data | SSIM (Structural Similarity index)
Noisy lifetime image | 12.9356 | 0.1209
Denoised lifetime image (at index 28) | 24.7218 | 0.5351
difference in PSNR is 11.7861 dB
Average (over 50 image) input PSNR = 14.4259 dB, denoised PSNR = 24.4810 dB with average difference of 10.0552 dB

## Slide 15: Summary of existing methods
Lifetime noise type is not same as intensity noise, but we used the same machine learning intensity denoising model to denoise the lifetime.
In the preprocess step: Image registration is required since the stage movement is more
Without image registration, denoising performance is minimal
Registration method: imregister with “rigid” method in MATLAB
Clearly, the denoising results with image registration shows there is an improvement of 9dB in PSNR between with and without denoising.
Artifacts: see the denoised lifetime images here

## Slide 16: Suggestions
Use the BPAE cells instead of mouse kidney (clear indication of improvement in lifetime)
Instead of denoise lifetime directly, denoise the G and S images and construct the lifetime using the following equation where is the modulation frequency (which is 80MHz in our experiment)
Questions:
  How to show G and S images have the Poisson dominated noise?
  What is the improvement in the denoised lifetime value compared to the old experiment?
  What are the limits of G and S used in the machine learning inference?
We used G limits are: -0.1 to 1.1 and S limits are: -0.1 to 0.6, clipping the the G and S images and pass through the machine learning inference model. and reconstructed back the lifetime from 0 to 10nsec range.
Notes: In the JOSA paper tau is the ratio of 2 variables (u1+sigma1*Y1) / (u2+sigma2*Y2) where Y1 and Y2 are 0 mean and unit variance auxiliary variables.

## Slide 17: Lifetime denoising – Option3
Use the BPAE cells instead of mouse kidney (clear indication of improvement in lifetime)
Instead of denoise lifetime directly, denoise the G and S images and construct the lifetime using the following equation where is the modulation frequency (which is 80MHz in our experiment)
Questions: How to show G and S images have the Poisson dominated noise?
  What are the limits of G and S used in the machine learning inference?
  What is the improvement in the denoised lifetime value compared to the old experiment?
We used G limits are: -0.1 to 1.1 and S limits are: -0.1 to 0.6, clipping the the G and S images and pass through the machine learning inference model and reconstructed back the lifetime from 0 to 10nsec range.
Hint: In the JOSA paper, we define the lifetime ( as the ratio of two variables U and V which has mean of and with variance of and . So can we assume U and V are Gaussian distribution? -> NO, for any unknown distribution, we just consider the statistics of 1st and 2nd order moments.
Notes: In the JOSA paper tau is the ratio of 2 variables (u1+sigma1*Y1) / (u2+sigma2*Y2) where Y1 and Y2 are 0 mean and unit variance auxiliary variables.

## Slide 18: Lifetime denoising: Option3
High-level block diagram of lifetime denoising is here
Image
denoising (Noise2Noise)
G and S
images
denoised
G and S images
Low-level block diagram of lifetime denoising is here
Image
denoising (Noise2Noise)
Noisy
G and S
images
denoised
G and S images
Pre
process
Post process
limit the G and S within valid range
restore the G and S images
Read
.tif file
mat
file

## Slide 19
Results: Noisy and denoised images (HSV)
(with registration) From G and S denoising
Full frame
ROI (100x100) at (position 225,300)
Noisy input
Denoised output
Target
Adjusted brightness in noisy intensity image

## Slide 20
Results: Noisy and denoised images (with registration) From G and S denoising
Denoised output
Target
Noisy input
range of tau: 0 to 10nsec

## Slide 21
Results: Noisy and denoised images (HSV)
(with registration) From G and S denoising
PSNR check?

## Slide 22: Select the mask area using ROIs
The area marked in blue circle is the noise region in the phasor diagram
get the mask of this noisy region and remaining image is the valid pixels
Export the segments and save this image as “noisy-region” where pixel value is zero. otherwise it is valid region with pixel value of 255.
Now compute the metric (PSNR) for the selected region only

## Slide 23: Lifetime denoising (metric on the valid region of pixels in lifetime)
Average PSNR of noisy input is 19.3551 dB
Average PSNR of denoised output is 27.6194
Improvement of 8.26dB (average over 50 images)
Clearly, PSNR of ROI is greater than PSNR of full image

## Slide 24
(a)
(b)
(c)
28 m
28 m
28 m